## Slide 1
PRODUCTION SYSTEM
Grid Origination
Intelligence Platform
Technical architecture, engineering trade-offs, and the Azure-native scale path
25.5M
SCED dispatch rows
11.7M
nodal price node-hours
1,109
ERCOT settlement nodes
340-bus
PyPSA network model
Amol Javahire · July 2026
Notes: Framing: this is a live production system I designed and built end-to-end — not a prototype. Today I want to cover three things: the architecture as built and why I made those calls, the engineering problems I hit and how I solved them, and how this scales onto the full Azure data platform for enterprise clients.

## Slide 2
CONTEXT
What the platform does
Power-market siting and PPA origination intelligence for corporate energy buyers
1
Screen
6,163 EIA-860 generators across ERCOT, CAISO and PJM, scored on 8 market-risk dimensions
2
Price
11.7M node-hours of real ERCOT day-ahead and real-time settlement prices, 1,109 nodes
3
Simulate
340-bus DC optimal power flow — curtailment, scarcity, transmission relief, battery arbitrage
4
Originate
Rank candidates by investment objective, model PPA/VPPA NPV with P10/P50/P90 Monte Carlo
Universe: EIA Form 860 (2025 vintage) operable generators >1 MW. Deployed and running on Azure.
Notes: Keep this brief — it's context, not the point of the deck. The one thing to land: every number on the screen traces to a primary regulator source, not an estimate. That matters for a deal team signing a 15-year PPA.

## Slide 3
AS-BUILT · TODAY
Current architecture
Deliberately lean: two compute processes, one managed database, no orchestration layer
Presentation
React 19 · Vite · Tailwind v4
Recharts · Leaflet
Static bundle via nginx
API tier
Express 5 on Node (PM2)
Drizzle ORM · Zod contracts
Reverse-proxies /pypsa
Solver
FastAPI · Uvicorn
PyPSA + HiGHS LP
Python 3.13 venv
Azure Database for PostgreSQL — Flexible Server + TimescaleDB
35 relational tables · 2 materialised views · 4.8 GB of 30 GB provisioned · hypertables on the 25.5M-row dispatch series
Single source of truth for the API, the solver, and the batch seeders — no duplicated state, no sync layer to keep honest.
Batch ingestion (Python · Polars)
ERCOT public API (OAuth ROPC + subscription key) · CAISO OASIS · EIA-930 / EIA-860 · HIFLD transmission · NOAA climate
Streaming ZIP → Polars → batched upsert. Idempotent seed logs make every run resumable.
Azure VM D2as_v6 (2 vCPU / 8 GB) · PM2 process manager · nginx TLS termination · GitHub-based deploy
Notes: The point of this slide is that the architecture is boring on purpose. Two processes, one database. No Kubernetes, no message bus, no orchestrator. For a single-tenant analytical product with batch ingestion and a synchronous solver, added distributed machinery would be cost and failure surface with no payoff. I'll show where that stops being true later in the deck.

## Slide 4
DATA ENGINEERING
Ingestion at scale
Every figure in the product traces to a primary regulator source
1
Authenticate
Azure AD B2C ROPC flow against ERCOT's public API, plus subscription key. Token cached and auto-refreshed.
2
Stream
ZIP archives pulled in 1 MB chunks — never materialised whole. Exponential backoff on the 30 req/min rate limit.
3
Parse
Polars reads CSV straight from the in-memory archive. Zero pandas: lower peak RSS, faster on wide frames.
4
Aggregate
15-minute settlement intervals rolled to hourly in-frame before any database round-trip.
5
Upsert
execute_values batches of 500–1,000 with ON CONFLICT DO UPDATE. Per-date seed log makes reruns free.
Result: 567 consecutive days of real-time nodal prices seeded with zero errors — 14.2M rows, fully resumable.
Notes: This is where I'd expect technical questions. The design constraint was a 2 vCPU / 8 GB VM against multi-gigabyte regulator archives. The answer was to never hold a full day in memory and to make every unit of work independently replayable. Polars over pandas was a deliberate memory decision, not a preference.

## Slide 5
TRADE-OFFS
Decisions and what they cost
Each choice bought something specific — and gave something up
Direct regulator APIs
over a data vendor
No licence cost, no vendor schema drift, full history control
We own auth, rate limits, and every format change
Polars
over pandas
Peak memory fell from ~7 GB to under 1 GB per ingest day
Smaller ecosystem; some libraries still return pandas
PostgreSQL + TimescaleDB
over a lakehouse
Sub-100 ms API reads, ACID, one engine to operate
Compression needs the Timescale licence Azure doesn't ship
Materialised views
over query-time aggregation
40,151-row rollup replaces a 25M-row scan per request
Staleness window; must refresh after each seed
Single VM
over AKS
~$150/mo all-in; no cluster to operate for one tenant
Vertical ceiling; no rolling deploy or self-healing
GAINED
GAVE UP
Notes: I want to be judged on the reasoning, not the stack. Every row here is a constraint-driven call I can defend, and every one has a real cost I accepted knowingly. The last row is the honest one: a single VM has no rolling deploy and no self-healing. That's fine for one tenant and unacceptable for a client platform — which is the bridge to the Azure section.

## Slide 6
PERFORMANCE ENGINEERING
A 22-minute query, and why
The capture-price materialised view — join geometry beat every other optimisation
BEFORE
Joined dispatch to prices on four derived columns —
year, month, day, hour-ending.
Planner could not hash a composite of four
expressions, so it nested-looped 25M rows.
22 min, never completed
AFTER
Pre-computed one Central-time timestamp per side,
joined on that single key.
Planner switched to a hash join. Same rows,
same result, one column instead of four.
Seconds
Three more that mattered
1
Disk spill
Aggregation exceeded work_mem and thrashed on BufFileRead. Raised to 512 MB for the build session — stayed in RAM.
2
Concurrency collapse
Three abandoned view builds ran simultaneously, starving each other. pg_stat_activity found them; terminating all but one fixed it.
3
Wrong denominator
A status endpoint ran COUNT(*) over 25M rows on every page load. Repointed to the 872-row seed log — instant.
Notes: This is my favourite slide because it's the one that shows how I actually work. The instinct is to reach for more hardware or more indexes. The real fix was reading the plan and realising a four-expression composite key can't be hashed. Same data, same result, 300x faster — from changing the shape of the join, not the size of the machine.

## Slide 7
SCALE TODAY
What is actually in the database
Row counts as deployed — not projections
Chart: 
| SCED dispatch | Nodal prices | ERCOT load | ERCOT fuel mix | CAISO hourly | Monthly rollup | Node stats | PJM stats
Rows | 25492166 | 11687827 | 174282 | 167190 | 65655 | 40151 | 19946 | 14336
Reading this
Log scale — the dispatch series is three orders of magnitude larger than the aggregates that serve it.
That gap is the whole performance strategy: the API almost never touches the big tables. It reads pre-aggregated views and monthly rollups, and the raw series exists for backtests and re-derivation.
The two materialised views are the seam. Everything above them is fast by construction.
4.8 GB
of 30 GB provisioned
<100 ms
typical API read
Notes: The log scale is the message. 25 million rows of dispatch, but the endpoints read tables in the tens of thousands. Designing that seam deliberately — rather than indexing the big table harder — is what keeps the product responsive on a 2 vCPU box.

## Slide 8
HONEST LIMITS
Where this architecture stops working
Fine for one tenant and one analyst team. Not fine for a client platform.
Single point of failure
One VM, one process manager. No rolling deploy, no self-healing, no zone redundancy. A bad restart is user-visible downtime.
Vertical ceiling
2 vCPU / 8 GB. Concurrent 340-bus solves already contend; multi-tenant load would not fit.
No governance plane
No data catalogue, no lineage, no classification, no access audit. Unacceptable for client data under NDA.
No orchestration
Seeders are cron and nohup. No dependency graph, no retry policy, no alerting on silent staleness.
Compression unavailable
Azure ships TimescaleDB under Apache licence — columnar compression needs the Timescale licence. Growth is linear.
Analytics coupled to OLTP
Heavy analytical scans compete with API reads on the same instance. One bad query degrades the product.
Notes: Leading with limitations is deliberate. I'd rather name the ceiling myself than have them find it. The important framing: none of these are mistakes — they're the correct trade for a single-tenant internal tool. They become blockers the moment this is client-facing, and that's precisely what the Azure target state addresses.

## Slide 9
TARGET STATE
Azure-native reference architecture
Same domain logic, enterprise-grade plane around it
Ingest & orchestrate
Fabric Data Factory pipelines · Event Hubs for streaming market telemetry · Functions for event-driven pulls
Store
OneLake (Delta Lake) as the single logical lake · PostgreSQL Flexible Server retained for OLTP + solver state
Model & serve
Fabric Warehouse for star-schema marts · Eventhouse / KQL for time-series at billions of rows · Direct Lake to Power BI
Reason
Microsoft Foundry — Agent Service on the Responses API, model catalogue, NL2SQL data agents over the semantic layer
Govern
Purview Unified Catalog · DSPM · AI-agent inventory and policy · Entra ID + workspace private link throughout
Run
AKS or Container Apps for the API and solver · Managed identities · Key Vault · Azure Monitor and Log Analytics
Fabric consolidates seven workloads on OneLake with one security model (Entra ID + Purview) and one capacity SKU (F-series).
Notes: Note what I did NOT do: I did not throw away PostgreSQL. The transactional store and the solver stay where they are strongest, and Fabric takes the analytical and AI surface. Ripping out a working OLTP engine to put everything in a lakehouse would be architecture-by-fashion.

## Slide 10
MIGRATION MECHANISM
The bridge: Fabric mirroring
Near-real-time replication from PostgreSQL into OneLake — no ETL to build or maintain
Azure PostgreSQL
Flexible Server
OLTP + PyPSA state
Stays authoritative
mirroring
OneLake
Delta Lake tables
Analytics-ready
Zero-copy to workloads
Consumers
Power BI Direct Lake
Foundry data agents
Notebooks / ML
Why this is the right seam
Analytical load leaves the OLTP instance entirely — no more heavy scans competing with API reads
No pipeline code to write, test, or monitor; mirroring is managed and continuous
Delta format is open — no lock-in on the storage layer
The 25.5M-row dispatch series becomes queryable at lakehouse scale without moving the product's source of truth
What I would still build
Medallion layering in OneLake — bronze raw archives, silver conformed prices, gold marts
Eventhouse / KQL for the tick-level series if we go below hourly granularity
A semantic model so NL2SQL agents query governed measures, not raw tables
Fabric Data Factory to replace cron, with dependency-aware retries and staleness alerts
Mirroring for Azure Database for PostgreSQL Flexible Server replicates continuously into OneLake without custom ETL.
Notes: This is the slide I'd want them to remember. The lean build was not a dead end — it's forward-compatible. Mirroring means the migration is additive rather than a rewrite: Postgres keeps serving the product while Fabric takes over analytics and AI. That de-risks the whole path.

## Slide 11
AZURE DATA STORES
Choosing the store, workload by workload
There is no single right database here — there are five right answers to five questions
STORE
BEST FIT
MY POSITION
PostgreSQL Flexible Server
Relational OLTP, PostGIS, solver state
What I use today. ACID, extensions, mirrors to Fabric.
Fabric Warehouse
Star-schema marts, T-SQL analytics
Serving layer for BI and governed measures.
Fabric Eventhouse (KQL)
Time-series at billions of rows
Where I would put 5-minute SCED and tick LMPs.
Azure SQL Database
Transactional apps, Hyperscale growth
Strong default if the team is T-SQL-first.
Cosmos DB
Global multi-tenant, low-latency documents
For per-client config and session state at scale.
Synapse Analytics
Existing dedicated SQL pools
Supported, but Fabric is the strategic target for net-new.
Synapse is not retired, but Microsoft positions Fabric for net-new investment; Synapse Data Explorer retired Oct 2025.
Notes: If they ask one 'do you really know Azure' question, it will be this one. The answer they want to hear is not a favourite product — it's workload-to-store reasoning. Note the Synapse row: knowing it's supported-but-not-strategic, and that Data Explorer specifically retired, is the kind of currency that separates real practice from a certification.

## Slide 12
FABRIC
Seven workloads, mapped to this platform
One capacity, one security model, one lake — the consolidation argument
1
Data Factory
Replaces cron seeders with dependency-aware pipelines and alerting
2
Data Engineering
Spark notebooks for the medallion transforms and backfills
3
Data Warehouse
T-SQL marts behind rankings, capture prices, congestion analytics
4
Real-Time Intelligence
Eventhouse for tick LMPs; Activator to fire on price or congestion events
5
Data Science
Load-forecast regression and curtailment models, tracked and versioned
6
Power BI
Direct Lake executive reporting with no import refresh cycle
7
Databases
Operational store option inside the same governance boundary
The pitch is not seven products — it is one bill, one identity model,
and no integration code between stages.
Notes: The consolidation argument is the real Fabric value proposition for a consulting engagement. Clients are not short of tools; they're short of integration budget. Fabric's answer is that the seams between ingestion, storage, warehousing, BI and AI are pre-built and governed by one model.

## Slide 13
AI LAYER
Microsoft Foundry — from chat box to governed agent
The platform already ships a Q&A copilot; Foundry is what makes it enterprise-safe
Today, in the product
An LLM with four tools: run_sql against any table, run_simulation into PyPSA, web_search, and a candidate lookup. Streams SQL, tables, charts and solver output back into the chat.
It works — but the model reaches raw tables directly, and nothing records what it saw.
On Foundry
Agent Service on the Responses API as a single entry point, model catalogue for routing cost against capability, and NL2SQL data agents querying a governed semantic model instead of raw SQL.
Every call is identity-bound, logged, and inventoried.
1
Governed retrieval
Agents query semantic models with row-level security, not ad-hoc SQL over production tables
2
Auditability
Prompt, response and tool-call lineage captured — the difference between a demo and something a regulated client will sign off
3
Model portability
Catalogue routing means swapping or tiering models is configuration, not a rewrite
4
Migration note
The legacy Assistants API retires 26 Aug 2026 — anything built on it needs to be on Agent Service before then
Azure AI Foundry was renamed Microsoft Foundry at Ignite 2025; Foundry Tools superseded the Azure AI Services brand.
Notes: Two things to land. First, I've already built the agentic pattern — tool-calling over a real database and a real solver — so this isn't theory. Second, the retirement date: knowing the Assistants API dies in August 2026 is exactly the kind of detail that decides whether a client's roadmap is real or aspirational.

## Slide 14
GOVERNANCE
Purview — the part clients actually buy
For energy clients under NDA, governance is the precondition, not the upsell
1
Unified Catalog
Authoritative inventory of every data asset, now GA. Lineage from regulator source to the number on a deal memo.
2
DSPM
Unified posture management across Microsoft and non-Microsoft sources, including data reached through AI apps and agents.
3
AI agent governance
Inventory of AI apps and agents with risk flags, sensitive-interaction counts, and per-agent policy — extends to Agent 365.
Why this is the commercial hinge
Market prices are public. The reason a utility or a corporate buyer cannot simply build this themselves is not the modelling — it is proving where every number came from, who touched it, and that no confidential position leaked into a model prompt.
Governance is what converts an analytical tool into something a client's risk committee will approve. It is also the layer a consulting firm is uniquely placed to implement, because it is organisational as much as technical.
Notes: This is the slide that connects the technical deck to the commercial one. Engineering directors sometimes treat governance as overhead. In energy trading and origination it is the gate — if you can't evidence lineage and prevent leakage, the deal team can't use your output regardless of how good the model is.

## Slide 15
PLATFORM ALTERNATIVES
Why Azure, honestly assessed
The case for Azure here is integration and governance — not raw capability on any single axis
Azure + Fabric
STRENGTHS
One governance model across data and AI
Mirroring removes ETL from the migration
Strongest fit where M365 and Entra already exist
TRADE-OFFS
Capacity SKU pricing needs active management
Fabric still maturing in places
AWS
STRENGTHS
Deepest primitive catalogue; Timescale compression available
Redshift / Athena mature
TRADE-OFFS
Governance is assembled from parts, not unified
Weaker M365 and Entra integration story
Databricks
STRENGTHS
Best-in-class Spark and ML lifecycle
Unity Catalog is genuinely strong
TRADE-OFFS
Another vendor plane to govern and bill
Overkill for hourly batch at this volume
Snowflake
STRENGTHS
Excellent warehouse ergonomics and elasticity
Clean separation of storage and compute
TRADE-OFFS
No native solver or agent runtime
Egress and cross-cloud cost coupling
Notes: I deliberately give the alternatives real strengths. Claiming Azure wins on every axis would tell them I haven't used the others. The defensible claim is narrower and stronger: for a client already on M365 and Entra, needing unified governance across data AND AI agents, Azure's integration story wins — and that is most large energy clients.

## Slide 16
EXECUTION
Phased migration — no big bang
Each phase ships value on its own and is independently reversible
1
Phase 1
Weeks 1–4
Turn on mirroring. Stand up OneLake, land the medallion bronze layer, point Power BI at Direct Lake. Product untouched.
2
Phase 2
Weeks 5–10
Containerise API and solver onto Container Apps. Managed identity, Key Vault, Azure Monitor. Retire the single-VM SPOF.
3
Phase 3
Weeks 8–14
Purview: catalogue, lineage, classification, DSPM. Prerequisite for any client data entering the platform.
4
Phase 4
Weeks 12–20
Fabric Data Factory replaces cron. Eventhouse for sub-hourly series. Semantic model built for agent access.
5
Phase 5
Weeks 18–26
Foundry Agent Service replaces the current copilot backend. NL2SQL over governed measures, full audit trail.
Sequencing rule: governance (Phase 3) must land before any client-confidential data enters the platform.
Notes: The sequencing is the argument. Mirroring first because it's additive and reversible. Governance before client data — non-negotiable. Agents last, because an agent over ungoverned data is a liability, not a feature. If they push on timeline, the honest answer is that Phase 1 is weeks and Phase 5 depends on how much semantic modelling the client's data needs.

## Slide 17
ECONOMICS
Cost shape across the phases
Indicative monthly run-rate — the step change is capacity, not compute
Chart: 
| As-built (VM + PG) | Phase 1 + Fabric F2 | Phase 2 + Container Apps | Phase 3 + Purview | Phase 5 + Foundry
Indicative $/month | 150 | 550 | 750 | 1050 | 1400
How to read it
The as-built figure is real: roughly $150/month for a D2as_v6 and a 30 GB Flexible Server.
The jump at Phase 1 is the Fabric capacity SKU — it is a reservation, not usage, so it must be sized and paused deliberately.
Figures are indicative for a single-tenant deployment in a US region. Any client proposal needs a sizing exercise against their actual concurrency, retention and DR requirements.
The honest headline: enterprise-grade costs roughly 10x lean. What you buy is availability, governance and multi-tenancy.
Indicative planning figures only — not a quote. Fabric F-SKUs are reserved capacity and can be paused.
Notes: Be explicit that these are planning numbers, not a quote — an engineering director will respect the caveat and distrust false precision. The substantive point is that the Fabric capacity SKU is a reservation, so FinOps discipline (right-sizing and pausing) is part of the architecture, not an afterthought.

## Slide 18
SUMMARY
What this demonstrates
1
Shipped, not slideware
A production system with 37M+ rows of regulator data, running today — designed, built and operated end-to-end.
2
Engineering judgment under constraint
Lean where lean was correct; every trade-off named, costed and defensible.
3
Depth where it counts
Query-plan level performance work, memory-bound ingestion design, and a documented silent-failure trap in the solver layer.
4
Azure fluency, current
Fabric, Foundry, Purview and the store-selection reasoning — including what changed in the last two release cycles.
5
A migration path clients can fund
Additive, reversible phases with governance sequenced before client data.
The platform is the evidence. The architecture reasoning is the transferable part.
Notes: Close on transferability. The energy domain is incidental — what moves to a client engagement is the reasoning: how to pick a store per workload, how to sequence a migration so it stays fundable and reversible, and how to put governance in front of AI rather than behind it.